## Slide 1: Mapping
COMSM4111 Robotic Systems
Delivered by:
Paul O’Dowd paul.odowd@bristol.ac.uk
Anonymous Feedback form:
https://forms.gle/PyQQy2mwzyATFmJW6
Padlet board (questions & comments):
http://padlet.com/paul_odowd1/1lhoodwv2fuc

## Slide 2: House Keeping
~60 People Assessed yesterday – well done, thank you!
Next weeks sign-up.
Group Declaration on BB.

## Slide 3
Week 1
Week 2
Week 3
Week 4
Week 5
Week 6
Week 7
Meet the Romi
Millis()
Motors
Encoders
Time & Speed
PID
Line Following
Kinematics
Finite State Machine
Lab Sessions / Sheets
Lectures
Assessment Op 1
Assessment Op 2
Assessment Op 3
Intro
Micro-controllers
Sensors & Actuators
Feedback Control 1
Feedback Control 2
PID Drop-In
Kinematics
Probabilistic Robotics
System
Architectures
Searching & Mapping
Path Planning
Sensor Fusion
Experimental Robotics
Toward
Assessment 2
Assessment 2 Briefing

## Slide 4: Mapping
Mapping Definition
Types of Maps
Key Challenges in Mapping
  Measurements
  Perceptual Aliasing
  Correspondence / Data Association Problem
  Example: Particle Filter Localisation
  Types of Environments
  Example: SLAM
  Exploration / Navigation

## Slide 5: Mapping: Definition
“Robotic mapping addresses the problem of acquiring spatial models of physical environments through mobile robots.”
Mapping algorithms tend to be greedy – e.g., maximise the discovery of information. (Do we want a slow, or partially mapped space?)
Robot has to move safely/efficiently (navigate, using a map)
Robot has to map (limited perceptual range incurs movement)

## Slide 6: Types of Maps
Topographical (Graphs)
Metric (Grids)

## Slide 7: A Caveat
Metric maps can be thought of as high-resolution topographical maps.
Or we often use a topographical system to navigate a metric map (waypoints).

## Slide 8: A Caveat
Topographical maps often reference metric representation (e.g., where is the vertex/node in a global coordinate system?)
Notes: Hybrid approaches

## Slide 9: Mobile Robotics Mapping
World-centric
Robot-centric
X = 100
Y = 200
X = -10
Y = 139
X = 30
Y = -439
?
Objects recorded in global coordinate space.
Sensor-measurements
recorded in global coordinate space.
Notes: Robot-centric: Using sensor-measurements recorded at different locations. If a list of known sensor-measurement locations are known, the approach doesn’t work so well with unknown environments. It is difficult to infer where you are in the gaps between sensor-measurements. However, the approach does work well as a system of landmarks to key localisation.
World-centric – world is “known”, so unknown sensor readings can be extrapolated to a position in the world. However, the world has to be known!

## Slide 10: Mapping
Mapping Definition
Types of Maps
Key Challenges in Mapping
  Measurements
  Perceptual Aliasing
  Correspondence / Data Association Problem
  Example: Particle Filter Localisation
  Types of Environments
  Example: SLAM
  Exploration / Navigation

## Slide 11: Key Challenges in Mobile Robotics Mapping

## Slide 12: Measurements
If the robot / object is fixed, we can cancel out the noise.
Measurements would be statistically independent.
Assumption that the localisation is error free.

## Slide 13: Measurements
If the robot / object is fixed, we can cancel out the noise.
Measurements would be statistically independent.
Assumption that the localisation is error free.

## Slide 14: Measurements
If the robot / object is fixed, we can cancel out the noise.
Measurements would be statistically independent.
Assumption that the localisation is error free.

## Slide 15: Measurements
If the robot / object is fixed, we can cancel out the noise.
Measurements would be statistically independent.
Assumption that the localisation is error free.

## Slide 16: Mapping: Definition
“Robotic mapping addresses the problem of acquiring spatial models of physical environments through mobile robots.”
Mapping algorithms tend to be greedy – e.g., maximise the discovery of information. (Do we want a slow, or partially mapped space?)
Robot has to move safely/efficiently (navigate, using a map)
Robot has to map (limited perceptual range incurs movement)

## Slide 17: Mapping
Mapping Definition
Types of Maps
Key Challenges in Mapping
  Measurements
  Perceptual Aliasing
  Correspondence / Data Association Problem
  Example: Particle Filter Localisation
  Types of Environments
  Example: SLAM
  Exploration / Navigation

## Slide 18: Perceptual Aliasing
A
B
C
?
How can we know whether the robot is at A, B, or C?

## Slide 19: Measurements
Pose Estimation / Localisation is another measurement subject to error.

## Slide 20: Measurements
The robot has to move and/or the environment is dynamic.
We need to make inferences from pose and state.
Measurements are effected by control error.
Measurements are statistically dependent.

## Slide 21: Mapping
Mapping Definition
Types of Maps
Key Challenges in Mapping
  Measurements
  Perceptual Aliasing
  Correspondence / Data Association Problem
  Example: Particle Filter Localisation
  Types of Environments
  Example: SLAM
  Exploration / Navigation

## Slide 22: Correspondence / Data Association Problem
“The problem of determining whether sensor measurement recorded at different points in time correspond to the same physical entity in the real world.”
Detected features are correct, but the map is skewed.
Long term accrual of error
Local/Immediate measurements can still be “trusted”, just misplaced.
Expectation-maximisation.
Notes: Expectation-maximisation

## Slide 23: Mapping
Mapping Definition
Types of Maps
Key Challenges in Mapping
  Measurements
  Perceptual Aliasing
  Correspondence / Data Association Problem
  Example: Particle Filter Localisation
  Types of Environments
  Example: SLAM
  Exploration / Navigation

## Slide 24: Example: Particle Filter Localisation
100
30
10
Sensor measurement “fingerprint”: 100, 30, 10

## Slide 25: Example: Particle Filter Localisation
100
30
10
Simulation Model
Hypotheses
Many “imaginary robots”

## Slide 26: Example: Particle Filter Localisation
100
30
10
Simulation Model
20,50,60
150,80,30
80,60,80
87,55,55
…
…
…
(n)

## Slide 27: Example: Particle Filter Localisation
100
30
10
Simulation Model
20,50,60
150,80,30
80,60,80
87,55,55
…
…
…
(n)

## Slide 28: Example: Particle Filter Localisation
100
30
10
Simulation Model
Repeat:
Adjust the Hypotheses
Move robots according to control model
Re-evaluate sensors

## Slide 29: Example: Particle Filter Localisation
100
30
10
Simulation Model
Repeat:
Adjust the Hypotheses
Move robots according to control model
Re-evaluate sensors

## Slide 30: Example: Particle Filter Localisation
100
30
10
Simulation Model
Repeat:
Adjust the Hypotheses
Move robots according to control model
Re-evaluate sensors

## Slide 31: Example: Particle Filter Localisation
100
30
10
Simulation Model
Probabilistic Localisation

## Slide 32: Example: Particle Filter Localisation
100
30
10
Simulation Model
Probabilistic Localisation

## Slide 33: Example: Particle Filter Localisation
Simulation Model

## Slide 34: Robotic Mapping
World-centric
Robot-centric
X = 100
Y = 200
X = -10
Y = 139
X = 30
Y = -439
?
Objects recorded in global coordinate space.
Sensor-measurements
recorded in global coordinate space.
Notes: Robot-centric: Using sensor-measurements recorded at different locations. If a list of known sensor-measurement locations are known, the approach doesn’t work so well with unknown environments. It is difficult to infer where you are in the gaps between sensor-measurements. However, the approach does work well as a system of landmarks to key localisation.
World-centric – world is “known”, so unknown sensor readings can be extrapolated to a position in the world. However, the world has to be known!

## Slide 35: Example: Particle Filter Localisation
100
30
10
Simulation Model
Probabilistic Localisation
Robot-centric
Measurements.
(dynamic)
World-centric
correlation.
(static)

## Slide 36: Mapping
Mapping Definition
Types of Maps
Key Challenges in Mapping
  Measurements
  Perceptual Aliasing
  Correspondence / Data Association Problem
  Example: Particle Filter Localisation
  Types of Environments
  Example: SLAM
  Exploration / Navigation

## Slide 37: Types of Environments
Static: Environment is fixed, structured, and of limited size. E.g., a laboratory.
  Can “solve mapping” relative to a World-centric localisation.
Dynamic: Environment and robot change over time. E.g., reality.
  Mapping relies on exploration, localisation, perception and map construction.

## Slide 38: Mapping
Mapping Definition
Types of Maps
Key Challenges in Mapping
  Measurements
  Perceptual Aliasing
  Correspondence / Data Association Problem
  Example: Particle Filter Localisation
  Types of Environments
  Example: SLAM
  Exploration / Navigation

## Slide 39: Simultaneous Localisation and Mapping (SLAM)
Given my location in the map,
what is my pose?
Given my pose,
where am I in the map?
X = 100
Y = 200
Map Updated
Pose Updated
Map information
Sensor information

## Slide 40: Sensor Fusion
A: Predicted Pose
B: Pose according to map
A: Predicted Map Feature
B: Map Feature according to pose

## Slide 41: Mapping
Mapping Definition
Types of Maps
Key Challenges in Mapping
  Measurements
  Perceptual Aliasing
  Correspondence / Data Association Problem
  Example: Particle Filter Localisation
  Types of Environments
  Example: SLAM
  Exploration / Navigation

## Slide 42: Exploration: Heuristics vs Randomisation
Heuristics:
“rules of thumb”
  Wall following
  Bug-algorithms
  Obstacle Avoidance
Exploration strategies
  Task / context dependent
Randomisation:
Low-cost (material, computation)
Some tasks require multiple passes (e.g. de-mining conflict zones).

## Slide 43: Exploration: Bostrophedon Planning (Greek, “ox-turning”)
http://planning.cs.uiuc.edu/node352.html
What to do if starting position is not at the edge of the space?
How to efficiently navigate back around obstructions?
3D printing infill algorithms?

## Slide 44: Exploration: Cellular Decomposition, Slab Method

## Slide 45: Exploration: Spanning Tree Covering
Y. Gabriely and E. Rimon. Spanning-tree based coverage of continuous areas by a mobile robot. Technical report, Dept. of Mechanical Engineering, Technion, Israel Institute of Technology, December 1999.

## Slide 46: Exploration: Wavefront
Set a start and goal location.
Create a gradient in a metric (grid) representation.
Greedily follow gradient to nearest neighbour, tracking visited cells.
Can be used to keep robot within safe distances of obstacles.
Potentially a path-planning problem (travelling salesman problem)

## Slide 47: Exploration: Sightseer Strategy
Terrain Acquisition
Attempts to find all objects within an enclosed space
Objects are ‘found’ once fully circumnavigated
Strategies are evaluated on objects found and total path length.

## Slide 48: Exploration: Rapid Information Gathering (RIG)
Typically uses PRM, RRT, etc.
Uses an ‘information metric’ to discern areas of interest / unexplored areas.

## Slide 49: Roomba Path
https://www.cnet.com/news/how-to-choose-the-best-robot-vacuum-for-your-home-roomba-neato-ecovacs-2019/

## Slide 50: Mint Path

## Slide 51: Mint Path (mopping)

## Slide 52: Mint Path (sweep)
https://www.youtube.com/watch?v=SusPRqU2W4M

## Slide 53: Mapping
Mapping Definition
Types of Maps
Key Challenges in Mapping
  Measurements
  Perceptual Aliasing
  Correspondence / Data Association Problem
  Example: Particle Filter Localisation
  Types of Environments
  Example: SLAM
  Exploration / Navigation

## Slide 54: Discussion
Key Challenges in Mapping
  Measurements
  Perceptual Aliasing
  Correspondence / Data Association Problem
  Example: Particle Filter Localisation
  Types of Environments
  Example: SLAM
  Exploration / Navigation
Static / Dynamic Obstacles
Odometry / kinematics
Motion Control
Path Planning
Exploration Strategies
Feature Characterisation
Uncertainty / Probability
Information Maximisation
Producing / Using a map