## Slide 1: Microcontrollers
COMSM4111 Robotic Systems
Delivered by:
Paul O’Dowd paul.odowd@bristol.ac.uk
Anonymous Feedback form:
https://forms.gle/PyQQy2mwzyATFmJW6
Padlet board (questions & comments):
http://padlet.com/paul_odowd1/1lhoodwv2fuc
Notes: This lecture is all about Time

## Slide 2: House Keeping
Booked Project rooms (floor space)
  Mon 5-6pm in both 1.11 & 1.11A MVB in weeks 1- 3, 5- 7, 9, 11 & 12
  Tue 5-6pm in 1.11MVB only in weeks 1- 4
  Tue 5-6pm in both 1.11 and 1.11A MVB in weeks 5- 7, 9, 10 & 12
  Thu 5-6pm in 1.11MVB only in weeks 1-7 & 9-12
  Fri 5-6pm in 1.11 & 1.11A MVB in weeks 1-3, 5-7 & 9-12
Not Booked:
  1.59QB and 1.60QB – Generally free Monday mornings, Wednesdays.
Can’t Upload?
  https://www.pololu.com/docs/0J69/9.1
  You need it to finish “Upload…” whilst the orange LED is still fading in/out.

## Slide 3
Week 1
Week 2
Week 3
Week 4
Week 5
Week 6
Week 7
Meet the Romi
Millis()
Motors
Encoders
Time & Speed
PID
Line Following
Kinematics
Finite State Machine
Lab Sessions / Sheets
Lectures
Assessment Op 1
Assessment Op 2
Assessment Op 3
Intro
Micro-controllers
Sensors & Actuators
Feedback Control 1
Feedback Control 2
PID Drop-In
Kinematics
Probabilistic Robotics
System
Architectures
A
Searching & Mapping
Path Planning
Sensor Fusion
Experimental Robotics
Toward
Assessment 2

## Slide 4: This Lecture:
Decomposing Problems
What is a microcontroller/computer?
Register Access
Using an Interrupt
Notes: The learning outcomes for this lecture are to:
Grasp a fundamental (deep) understanding of how we use microcontroller peripherals like Timers, Interrupts, etc.
  This means knowing something of how computers work…
  …and why we then write software the way we do.
Ordinarily, this is difficult to grasp by ‘just doing it’, it needs to be taught.
We will also looks at how it is done on Arduino (surface level understanding).
You should be able to apply all this in the lab session.
Hopefully, the strange software will make more sense after this.

## Slide 5: Reminder: Assessment 1
Notes: These are the tasks our robot has to complete:
Move in a straight line (30 points)
Find the start of a line of follow it
Determine when you have reached the end of the line (5 points)
Return to and stop at the starting location

## Slide 6: Decomposing the Problem
Line Following
Finding Line
Joining Line
Following Line
Identifying Line Terminus
Driving Straight
Calibrating Line Sensors
Catching Loss of Line
Confidence in Line End
Sense of Time?
Sense of Line Continuity?
Going Home
Notes: For each,
what do we need to know to achieve them?
What can we use to achieve them (how)?

## Slide 7: Decomposing the Problem
“Human Perspective”
“Robot Perspective”
(semantic / behavioural)
(numerical)
Line Following
Finding Line
Joining Line
Following Line
Identifying Line Terminus
Driving Straight
Calibrating Line Sensors
Catching Loss of Line
Confidence in Line End
Sense of Time?
Sense of Line Continuity?
Going Home
Notes: For each,
what do we need to know to achieve them?
What can we use to achieve them (how)?

## Slide 8: Decomposing the Problem
“Human Perspective”
“Robot Perspective”
(semantic / behavioural)
(numerical)
Line Following
Finding Line
Joining Line
Following Line
Identifying Line Terminus
Driving Straight
Calibrating Line Sensors
Catching Loss of Line
Confidence in Line End
Sense of Time?
Sense of Line Continuity?
Going Home
What we want to observe
Description in code
Notes: For each,
what do we need to know to achieve them?
What can we use to achieve them (how)?

## Slide 9: Dependency of a Robotic System
Read Sensors / Drive Actuators
Closed Loop Motion Control
Position Tracking
Mission Planner
( on time )

## Slide 10: This Lecture:
Decomposing Problems
What is a microcontroller/computer?
Register Access
Using an Interrupt
Notes: The learning outcomes for this lecture are to:
Grasp a fundamental (deep) understanding of how we use microcontroller peripherals like Timers, Interrupts, etc.
  This means knowing something of how computers work…
  …and why we then write software the way we do.
Ordinarily, this is difficult to grasp by ‘just doing it’, it needs to be taught.
We will also looks at how it is done on Arduino (surface level understanding).
You should be able to apply all this in the lab session.
Hopefully, the strange software will make more sense after this.

## Slide 11: What is a microcontroller / computer?
Notes: Ask the audience for some definitions of computers (set context):
What they are
What they do
Why they are useful.

## Slide 12: What parts build a computer?
Notes: Ask audience to outline components of a computer, in order to break down ‘computer’ into the idea of a computer being made of many parts.

## Slide 13: AVR Atmega 32u4
Notes: This is the block diagram for the 32u4 – which is the microcontroller we are working with.
What is the difference between a micro-controller and a micro-processor?
The Printed Circuit Board this chip is mounted on fits within the Arduino ecosystem/community, e.g., the pins of the microcontroller are labelled with the definitions created by Arduino. Therefore, we can use Arduino libraries and the IDE.
But we are going to take a deeper look, and write some of our own code for this chip.

## Slide 14: AVR Atmega 32u4
Notes: This red circle is the electronic symbol for a Crystal.
The Crystal circuit creates a precise oscillation, for this board, 16Mhz.
What would happen if the clock speed were to vary?

## Slide 15
Quarts:
Piezo effect
16Mhz
Notes: This is where the crystal is on the Romi board.

## Slide 16
16Mhz
Notes: And this is the Microcontroller Chip (34u2)

## Slide 17
16Mhz
Notes: Why might the Crystal and Microcontroller be so close to each other?
You will almost always find it to be this way.

## Slide 18: AVR Atmega 32u4
Notes: Lets look at the block diagram again.
All these parts, all the blocks, are inside the chip.

## Slide 19
Notes: The block diagram fits inside the chip.

## Slide 20
Notes: And the rest of the board is mostly electronics to support the chip, and at a physical size that is useful so we can plug things in.

## Slide 21: Analog and Digital
pinMode( n, INPUT );
pinMode( n, OUTPUT );
analogRead( );
analogWrite( );
digitalRead( );
digitalWrite( );
Tell the microcontroller the ‘direction’ of a pin.
We need to configure the microcontroller in setup() {…}
Transform a continuous voltage into a digital encoding.
Transform a digital encoding into a continuous voltage.
Measure voltage against threshold, true or false (HIGH/LOW)
Set voltage HIGH/LOW

## Slide 22: Quick Look at the Analog-to-Digital Converter (ADC)

## Slide 23: AVR Atmega 32u4
Notes: Lets look at the block diagram again.
All these parts, all the blocks, are inside the chip.

## Slide 24
8-Bit ADC ?
10-Bit ADC ?
?
?
?
?
?
analogRead( A0 );
01001101
( 77 )

## Slide 25: Closer look at the Digital Pins.

## Slide 26: AVR Atmega 32u4
Notes: This part of the diagram is labelled as ‘PORTF Drivers’.
It represents a set of pins on the chip.

## Slide 27
Notes: On the board, these pins are then wired (printed circuit board traces) to a set of big pins on the board.
Really, the circuit board is mapping the microchip to physical pins that are large enough for us to use!
If you look closely, you can even see the lines on the circuit board.

## Slide 28
This bit is the
‘computer’.
We can think of the
rest as peripherals.
Notes: Looking at the Block diagram again:
This green area is really the ‘computer’ – the bit which manipulates numbers (0’s and 1’s).
Does anyone know what an ALU is?
…Stack?
If you want to know more, a good place to start is the Von Neumann architecture.
https://en.wikipedia.org/wiki/Von_Neumann_architecture

## Slide 29
Central Processing Unit
(transforming numbers)
INPUT
OUTPUT
Notes: We can think of using a computer as:
Taking in ‘input’
Making some transformation of inputs.
  Note, computers can also ‘remember’ as part of the transformation process.
Creating ‘outputs’.

## Slide 30
Central Processing Unit
(transforming numbers)
INPUT
OUTPUT
( a robot? )
Notes: If the output of the computer has an effect on the input, does this automatically make it a robot?
If not, what is a key distinction?

## Slide 31
Central Processing Unit
(transforming numbers)
INPUT
OUTPUT
Notes: For Robots, we expect to have sensors as inputs, and actuators as outputs.
Microcontrollers are everywhere.
The Shape Rangefinder on the left has its own microcontroller to process the infrared signal.
This idea of [ input -> process -> output ] happens within most devices.

## Slide 32
From the point of
view of the CPU,
All of the blue is
input and output
(and it is all digital)
Notes: The blue bit is all peripherals – extra devices the computer can use.
These include:
Analog to Digital Converter (ADC)
Temperature Sensor
Timers, Counters & Interrupts
Data Ports (pins to read or write values)

## Slide 33
https://commons.wikimedia.org/wiki/File:2-chinese-room.jpg, accessed 10/12/18
Notes: We can think of a computer as a bit like a translation machine.
It takes numbers as inputs.
It performs transformations on the numbers using ‘operation codes’ (which we program)
It produces numerical outputs, represented (or stored) as electronic signals/states.

## Slide 34: This Lecture:
Decomposing Problems
What is a microcontroller/computer?
Register Access
Using an Interrupt
Notes: The learning outcomes for this lecture are to:
Grasp a fundamental (deep) understanding of how we use microcontroller peripherals like Timers, Interrupts, etc.
  This means knowing something of how computers work…
  …and why we then write software the way we do.
Ordinarily, this is difficult to grasp by ‘just doing it’, it needs to be taught.
We will also looks at how it is done on Arduino (surface level understanding).
You should be able to apply all this in the lab session.
Hopefully, the strange software will make more sense after this.

## Slide 35: Register Access

## Slide 36
Example:
Setting a pin to output/input with Arduino code
Notes: This code uses the functions defined by the Arduino environment.
We will explore what is going on beneath them.

## Slide 37
Notes: To read and write to pins, the CPU has to activate peripheral hardware.
The block I have highlighted blue is repeated in this block diagram.
The chip is 8bit, which means that most of the hardware is accessed and controlled using 8bits of memory.
The block I have highlighted blue controls 8 physical pins on the chip.

## Slide 38: Inside the manual…

## Slide 39
Notes: To read and write to pins, the CPU has to activate peripheral hardware.
The block I have highlighted blue is repeated in this block diagram.
The chip is 8bit, which means that most of the hardware is accessed and controlled using 8bits of memory.
The block I have highlighted blue controls 8 physical pins on the chip.

## Slide 40
Where the value to
read or write
is set and stored.
Where the direction
in or out
is set and stored.
Circuit to
write or buffer
voltages
Actual pins on the chip
Notes: Here we can see a closer look at the block which controls the pins.
We can see that there are registers associated to this block.
A register is a portion of memory that is used to control the electronics (hardware).

## Slide 41
Where the value to
write
is set and stored.
Notes: This register stores the state we wish the pin to be in if it is an output.

## Slide 42
Where the direction
in or out
is set and stored.
Notes: This register configures a pin to be either input, or output.

## Slide 43
Where the value
read
stored.
Notes: Another register is located here which stores the last value read as an input.
Why might input and output states be stored in different registers?

## Slide 44
8 bits that match
Up to 8 pins
Input or
Output (?)
Input
High or low (?)
Output high
or low (?)
Notes: We can see all three registers used to perform the Arduino functions:
pinMode( );
digitalWrite( );
digitalRead( );

## Slide 45
Notes: So, a register is a place in memory. Where?
If we want, we can find out in the manual.
These memory addresses are fixed! They are set by the manufacturer.
Generally, it is better to use them by referring to keyname they are given, like PORTD, DDRD, PINE etc. These keywords reference the address.

## Slide 46
Direct access in C using a pointer:
Notes: If we were going to access them directly, this is the type of C syntax we would need to use.
We won’t go further into this.

## Slide 47
Notes: Microcontrollers have a big block of memory.
A portion of this is reserved for the control registers.
In a more sophisticated Integrated Development Environment (IDE), it is possible to view the memory blocks directly.
So memory is essentially a big table of numbers.
Some are registers, the rest are program space.

## Slide 48
Notes: Chips are manufactured on big silicon wafers like this.
http://kremesti.com/semiconductor_chip_manufacturing.html
Image from: https://www.istockphoto.com/gb/photos/silicon-chip-wafer?mediatype=photography&phrase=silicon%20chip%20wafer&sort=mostpopular

## Slide 49
Notes: A closer look shows something of their structure.

## Slide 50
Notes: Notice the two large blocks – these are probably the memory of the chip.
Memory is just large arrays of millions of transistors, like a look up table.

## Slide 51
What we had before:
Notes: This is the code we had before.

## Slide 52
The same thing, with direct access to registers:
Notes: This is how to achieve the same thing by writing 0’s and 1’s into the registers themselves.
Generally this is not advised.
The Arduino environment is so successful because code written in Arduino (generally) works on all their different boards.
This is because calls like digitalWrite() have a lot of clever code behind them to make sure that different machine code is generated for different chips.
However it should be interesting to know what is going on when you make a call like digitalWrite() – it is not magic. Those 0’s and 1’s are turning transistor circuits on and off. If you want, you can find the exact memory locations in the manual!

## Slide 53: This Lecture:
Decomposing Problems
What is a microcontroller/computer?
Register Access
Using an Interrupt
Notes: The learning outcomes for this lecture are to:
Grasp a fundamental (deep) understanding of how we use microcontroller peripherals like Timers, Interrupts, etc.
  This means knowing something of how computers work…
  …and why we then write software the way we do.
Ordinarily, this is difficult to grasp by ‘just doing it’, it needs to be taught.
We will also looks at how it is done on Arduino (surface level understanding).
You should be able to apply all this in the lab session.
Hopefully, the strange software will make more sense after this.

## Slide 54
Notes: The graph on the left could be various sensor information:
Sound
Speed of a robot
Radio signal
We can reconstruct this signal using a digital representation, like on the right.
It is important the representation is consistently timed.

## Slide 55
Notes: We can see here, if the samples are irregularly timed, we lose important information.
This loss of information will result in error that integrates over time.
If the graph on the left was the speed of the robot, then we would quickly lose track of our integrated position.

## Slide 56
CPU is going
setup and use
Timer3
Notes: Fortunately, a microcontroller has a unit designed to run code at precise time intervals.
They are called timers.

## Slide 57
Timer3 is then
going to interrupt
the CPU’s normal
operation with a set
frequency
…Hey!
Notes: A timer keeps track of time, and then raises an interrupt flag, which causes the microcontroller to run an Interrupt Service Routine.
You can think of an ISR as a piece of code that runs like a background task.

## Slide 58
Notes: This is the Arduino sketch we have seen so far.
It has a setup which runs once.
And a loop which iterates itself forever.

## Slide 59
ISR( TIMER3_COMPA_vect ) {
instruction 1;
instruction 2;
…
}
Notes: An interrupt can break the flow of the loop to run important code.

## Slide 60
Loop()
Code
Time
1.5 Seconds
0 Second
Loop()
Code
Interrupt Service
Routine
Interrupt Service
Routine
Loop()
Code
Interrupt Service
Routine
…Hey!
…Hey!
…Hey!
CPU
Timer3
@2Hz
1, 2, 3, 4, 5, 6, 7,
8, 9, 10, 11, 12,
13, 14, 15, 16, 17
16Mhz
Notes: The Timer is attached to the CPU, and so it uses the 16mhz clock of the cpu.
The timer has to be configured to run either at 16mhz, or slower.

## Slide 61: Prescaler
0 Hz
16 MHz
2 MHz
250 KHz
62.5 KHz
15.625 KHz
?
?
clk I/o
= 16 MHz
Timer Frequency:
ftimer = f i/o / prescaler

## Slide 62
TCCR3B = 0B00000101

## Slide 63
TCCR3B = 1024;

## Slide 64: Setting a specific frequency
0 Hz
16 MHz
2 MHz
250 KHz
62.5 KHz
15.625 KHz
Timer Frequency:
?

## Slide 65: Setting a specific frequency
16 MHz
2 MHz
250 KHz
62.5 KHz
15.625 KHz
Prescaled Timer Frequency:
?
( count up to a value we specify )
ISR

## Slide 66: Setting a specific frequency
16 MHz
2 MHz
250 KHz
62.5 KHz
15.625 KHz
Prescaled Timer Frequency:
Another Register:
OCR3A
16 Bits
Max value: 65,536

## Slide 67
ftimer = f i/o / prescaler

## Slide 68
ftimer = f i/o / prescaler
fdesired = ftimer / OCR3A

## Slide 69
ftimer = f i/o / prescaler
fdesired = ftimer / OCR3A
OCR3A = ftimer / fdesired

## Slide 70: Example

## Slide 71: Prescaler
0 Hz
16 MHz
2 MHz
250 KHz
62.5 KHz
15.625 KHz
?
?
clk I/o
= 16 MHz
Timer Frequency:
ftimer = f i/o / prescaler

## Slide 72
2000000 = 16000000 / 8
fdesired = ftimer / OCR3A
OCR3A = 2000000 / 37900
OCR3A = 52.7
Max = 65536
53
Min = 0
OCR3A
OCR3A = ftimer / fdesired

## Slide 73
Loop()
Code
Time
0 Second
Loop()
Code
Interrupt Service
Routine
Interrupt Service
Routine
Loop()
Code
Interrupt Service
Routine
…Hey!
…Hey!
…Hey!
CPU
Timer3
2Mhz
Prescale 8
OCR3A = 53
1, 2, 3, 4, 5, 6, 7,
8, 9, 10, 11, 12,
13, 14, 15, 16, 17
16Mhz
Blink LED
@37.9Khz
Notes: The Timer is attached to the CPU, and so it uses the 16mhz clock of the cpu.
The timer has to be configured to run either at 16mhz, or slower.

## Slide 75
Loop()
Code
Time
0 Second
Loop()
Code
Interrupt Service
Routine
Interrupt Service
Routine
Loop()
Code
Interrupt Service
Routine
…Hey!
…Hey!
…Hey!
CPU
Wheel
Rotation
1, 2, 3, 4, 5, 6, 7,
8, 9, 10, 11, 12,
13, 14, 15, 16, 17
16Mhz
Notes: The Timer is attached to the CPU, and so it uses the 16mhz clock of the cpu.
The timer has to be configured to run either at 16mhz, or slower.

## Slide 76: To Summarise

## Slide 77: Dependency of a Robotic System
Track Wheel Rotation (Labsheet 4)
PID Feedback Control (Labsheet 6)
Position Tracking (Labsheet 8)
Mission Planner
( on time )

## Slide 78: Dependency of a Robotic System
Track Wheel Rotation (Labsheet 4)
PID Feedback Control (Labsheet 6)
Position Tracking (Labsheet 8)
Mission Planner
( on time )
(time known)

## Slide 79: Dependency of a Robotic System
Track Wheel Rotation (Labsheet 4)
PID Feedback Control (Labsheet 6)
Position Tracking (Labsheet 8)
Mission Planner
( on time )
(time known)
In good time

## Slide 80: Dependency of a Robotic System
Track Wheel Rotation (Labsheet 4)
PID Feedback Control (Labsheet 6)
Position Tracking (Labsheet 8)
Mission Planner
( on time )
(time known)
In good time
When Necessary

## Slide 81: Questions
Anonymous Feedback form:
https://forms.gle/PyQQy2mwzyATFmJW6
Padlet board (questions & comments):
http://padlet.com/paul_odowd1/1lhoodwv2fuc